## Slide 1: Basic Military Communications

## Slide 2: Objectives
Teach soldier minimum skills needed:
To operate basic communication equipment
To transmit and receive messages by wire and radio

## Slide 3: Phonetic Alphabet and Numerals

## Slide 4: Numeral Pronunciation
44 FOW-ER FOW-ER
90 NIN-ER ZE-RO
136 WUN TREE SIX
500 FIFE ZE-RO ZE-RO
1200 WUN TOO ZE-RO ZE-RO
1478 WUN FOW-ER SEV-EN AIT
7000 SEV-EN TOU-SAND
16000 WUN SIX TOU-SAND
812681 AIT WUN TOO SIX AIT WUN
Viewgraph 3A

## Slide 5: Some Common Prowords Listed Alphabetically
PROWORD EXPLANATION
ALL AFTER I refer to all of the message that follows...
ALL BEFORE I refer to all of the message that precedes...
BREAK I now separate the text from other parts of the message.
CORRECTION There is an error in this transmission. Transmission will continue with the last word correctly transmitted.
GROUPS This message contains the number of groups indicated by the numeral following…
I SAY AGAIN I am repeating transmission or part indicated.
I SPELL I shall spell the next word phonetically.
Viewgraph 4

## Slide 6
MESSAGE A message that requires recording is about to follow. (Transmitted immediately after the call.) This proword is not used on nets primarily employed for conveying messages. It is intended for use when messages are passed on tactical or reporting net.
MORE TO Transmitting station has additional traffic for the
FOLLOW receiving station.
OUT This is the end of my transmission to you and no answer is required or expected.
OVER This is the end of my transmission to you and a response is necessary. Go ahead: transmit.
RADIO CHECK What is my signal strength and readability, i.e., How do you hear me?
ROGER I have received your last transmission satisfactorily, radio check is loud and clear.
Prowords (Cont’d)
Viewgraph 4A

## Slide 7
SAY AGAIN Repeat all of your last transmission. Followed by identification data means “repeat - (portion indicated).”
THIS IS This transmission is from the station whose designator immediately follows.
TIME That which immediately follows is the time or date-time group of the message.
WAIT I must pause for a few seconds.
WAIT-OUT I must pause longer than a few seconds.
WILCO I have received your transmission, understand it, and will comply, to be used only by the addressee. Since the meaning of ROGER is included in that of WILCO, the two prowords are never used together.
WORD AFTER I refer to the word of the message that follows.
WORD BEFORE I refer to the word of the message that precedes.
Prowords (cont’d)
Viewgraph 4B

## Slide 8: CALL SIGN PRONUNCIATION
A2D28A ALPHA TOO DELTA TOO AIT ALPHA
C8T11B CHARLIE AIT TANGO WUN WUN BRAVO
L7I09C LIMA SEVEN INDIA ZERO NINER CHARLIE
L7Z09D LIMA SEVEN ZULU ZERO NINER DELTA
B0F07E BRAVO ZERO FOXTROT ZERO SEVEN ECHO
R7G28F ROMEO SEVEN GOLF TOO AIT FOXTROT
T3F07G TANGO TREE FOXTROT ZERO SEVEN GOLF
A6C18H ALPHA SIX CHARLIE WUN AIT HOTEL
S8C15J SIERRA AIT CHARLIE WUN FIFE JULIETTE
TELEPHONE NUMBER PRONUNCIATION
SERVANT 101 SERVANT WUN ZERO WUN
BLACKJACK 386 BLACKJACK TREE AIT SIX
COBRA 472 COBRA FOWER SEVEN TOO
Viewgraph 5

## Slide 9: Telephone Set TA-1/PT
Viewgraph 6
RECEIVER
VISUAL INDICATOR
GENERATOR LEVER
TRANSMITTER
RIDGE
BUZZER VOLUME
CONTROL KNOB
PRESS-TO-
TALK
SWITCH
BINDING POSTS
LIVE WIRES

## Slide 10: Brief Written Message
(Telephone rings) blackjack 103
This is blackjack 156 - -
observe enemy patrol approaching perimeter. over.
Continue to observe, out.
Viewgraph 7

## Slide 11: Telephone Set TA-312/PT (Top View)
Viewgraph 7
Viewgraph 8
SELECTOR SWITCH
BUZZER
VOLUME CONTROL
RECEPTACLE
CONNECTOR
U-79/U
HOOK
SWITCH

## Slide 12: Telephone Set TA-312/PT (Top View with Battery Compartment Open)
Viewgraph 7
Viewgraph 9
CARRYING CASE
RETAINING STRAP
(OPEN)
BATTERY COMPARTMENT
COVER LATCH (TURN
CLOCKWISE TO OPEN)
BATTERIES BA-30
GASKET
BATTERY
COMPARTMENT
COVER
COVER
TERMINAL

## Slide 13: Telephone Set TA-312/PT (Side View)
Viewgraph 7
Viewgraph 10
CARRYING
STRAP
SLIDE FASTENER
(CLOSED)
SNAP FASTENER
GENERATOR
HAND RINGING
G-42A/PT
TELEPHONE SET CASE
CY-122B/PT
BUZZER BZ
23/PT
CARRYING
STRAP

## Slide 14: Technical Characteristics of AN/PRC-77
FREQUENCY RANGE:
LOW BAND 30.00 TO 52.95
HIGH BAND 53.00 TO 75.95
NUMBER OF CHANNELS: 920
TRANSMITTER OUTPUT POWER 1.0 TO 4.0 WATTS
DISTANCE RANGE 5 MILES (8 KILOMETERS)
POWER SOURCE BATTERY, DRY BA-4386/U OR BA398/V
BATTERY LIFE 60 HOURS (WITH 9:1 RECEIVE-TRANSMIT RATIO)
Viewgraph 11

## Slide 15: Send a Radio Message
DELTA 8 1 THIS IS ZULU 9 4, MESSAGE, OVER.
THIS IS DELTA 8 1, ROGER, OVER.
THIS IS ZULU 9 4 - ENEMY RIFLE SQUAD MOVING SOUTH ALONG WOODLINE, GRID NOVEMBER ALPHA 772957, I’M CONTINUING TO OBSERVE, TIME 0920, OVER.
THIS IS DELTA 8 1, ROGER, OUT.
Viewgraph 12
(This viewgraph not noted in TSP)

## Slide 16: SINCGARS, RT-1523 C/U
Viewgraph 13
SINCGARS - ICOM
RECEIVER - TRANSMITTER

## Slide 17: SINCGARS, RT-1439 C/U
Viewgraph 14
RECEIVER - TRANSMITTER (FRONT)
AUD/FILL
(AUDIO FILL)
VOL(VOLUME)
WHSP (WHISPER)
AUD/DATA
(AUDIO DATA)
DATA
KEYBOARD
DIM
MODE
FCTN
(FUNCTION)
RXMT
(RETRANSMIT)
KEYBOARD
DISPLAY
SIG
(SIGNAL)
CHAN
(CHANNEL)
RF
ANT
(ANTENNA)

## Slide 18: SINCGARS, P1 System Connector
Viewgraph 12
Viewgraph 15
P1
P1 Systems connector. connects to systems connector on battery box.

## Slide 19: SINCGARS, Battery/Battery Box
Viewgraph 16
BATTERY
BOX
BINDING POST
CONNECTOR
P1 RT SYSTEM
CONNECTOR
HOLDING
BATTERY DECAL
(BOTTOM OF RT)
BATTERY
LATCHES
RT

## Slide 20: SINCGARS, Components
Viewgraph 17
MANPACK
ANTENNA
HANDSET
RUCKSACK